## Slide 1: Experiment-10
Interface LCD with Raspberry Pi 4

## Slide 2: 9. Interface LCD with Raspberry Pi 4
import smbus
import time
# Define LCD parameters
LCD_WIDTH = 16 # Maximum characters per line
# Define some device parameters
I2C_ADDR = 0x27 # I2C device address
LCD_CHR = 1 # Mode - Sending data
LCD_CMD = 0 # Mode - Sending command
LCD_LINE_1 = 0x80 # LCD RAM address for the 1st line
LCD_LINE_2 = 0xC0 # LCD RAM address for the 2nd line
LCD_BACKLIGHT = 0x08 # On
# LCD_BACKLIGHT = 0x00 # Off
ENABLE = 0b00000100 # Enable bit
# Timing constants
E_PULSE = 0.0005
E_DELAY = 0.0005
# Open I2C interface
bus = smbus.SMBus(1) # Rev 2 Pi uses 1
def lcd_byte(bits, mode):
# Send byte to data pins
bits_high = mode | (bits & 0xF0) | LCD_BACKLIGHT
bits_low = mode | ((bits << 4) & 0xF0) | LCD_BACKLIGHT
# High bits
bus.write_byte(I2C_ADDR, bits_high)
lcd_toggle_enable(bits_high)
# Low bits
bus.write_byte(I2C_ADDR, bits_low)
lcd_toggle_enable(bits_low)
def lcd_toggle_enable(bits):
# Toggle enable
time.sleep(E_DELAY)
bus.write_byte(I2C_ADDR, (bits | ENABLE))
time.sleep(E_PULSE)
bus.write_byte(I2C_ADDR, (bits & ~ENABLE))
time.sleep(E_DELAY)
def lcd_string(message, line):
# Send string to display
message = message.ljust(LCD_WIDTH, " ")
lcd_byte(line, LCD_CMD)
for i in range(LCD_WIDTH):
lcd_byte(ord(message[i]), LCD_CHR)
if __name__ == '__main__':
try:
while True:
lcd_string("Hello, World!", LCD_LINE_1)
lcd_string("Raspberry Pi", LCD_LINE_2)
time.sleep(2) # 2 second delay
lcd_string("LCD Interfacing", LCD_LINE_1)
lcd_string("with Python", LCD_LINE_2)
time.sleep(2) # 2 second delay
except KeyboardInterrupt:
pass
finally:
lcd_string("", LCD_LINE_1)
lcd_string("", LCD_LINE_2)
time.sleep(2)